VENDESI L’AEREO DEI RECORDS

GIRO DEL MONDO CONTROVENTO CON DOPPIA TRAVERSATA DELL’EQUATORE.

MOLTE TRAVERSATE OCEANICHE COMPRESO IL PERIPLO DELL’ATLANTICO CON DOPPIA TRAVERSATA SUD E NORD MASSIMA DISTANZA NON STOP OVER OCEANO PACIFICO SAN FRANCISCO USA HONOLULU HAWAI ifr 4100 km.

ENDURANCE

with tip flint aero gals 120 No wind MAX RANGE 1350 NAUTICAL MILES

with ferry tanks gals 270 No wind MAX RANGE 2900 NAUTICAL MILES

1980 CESSNA TURBO CENTURION II –

MODEL T 210 N

SERIAL N.21063796

REGISTRATION I-BBTT

- AIRFRAME

3160 hrs TT AF SINCE NEWS

- ENGINE

Powerplant: teledyne continental motors TS10-520-R4B 310

640 hrs SINCE MAJOR OVERHAUL – TBO 1600 hrs

- PROP(S)

Hartzell PHC-J3YF-IRF/F7663D-2Q SPECIAL

Noise level 77.4 OLB (A)

# TOP OVERHAUL JUNE 2009

- LANDING GEAR

# TOP OVERHAUL JUNE 2009

- ADDITIONAL EQUIPMENT

- Turbo plus options

- SPI engine data management EDM 700

- Dual vacuum

- Dual altimeters

- Dual glide slope indicators

- Dual alternetor control units

- 4 place intercom

- 6 seats

- Kit Robertson stol stall speed 54 kias

- Electric trim

- Speed brakes

- Wing tip aux FLINT AERO 33 US gals

- Efis sandel 3308EHSI

- HF radio icom with aerial

- Special ferry tank GLOBE AERO Lakeland n.2 capacity 74+74 US gals

- Interior

6 place leather seats

New vacuum pump

New electric system

New turbo gami jectors GT 14 C SN 8870 increase endurance

AVIONICS/RADIO

New king KMA 24 audio panel with 3 LMB

New king Kx 165

New king Kx 155

New autopilot S-TEC FIFTYFIVE SYSTEM

New ST 645 REMOTE ANNUNCIATOR

New ST-361 P SINGLE CUE FLIGHT DIRECTORY STAB/PICH OFF

New ST 360 ALTITUDE SELECTOR/ALERT SYSTEM

New STORMSCOPE 3M-WX-10°

GPS king KLN 89B navigation system couplins autopilot

DME king KN 62 A

ADF King KR 87

Rmi KING ki 229

Transponder KT 76A

Transponder KT 76C

## Radar RDR 160 colour Radar System

EFIS SANDEL SN 3308 COLOR MAP HSI

SPI EDM 700 engine data management fuel flow management system

Always hangared

No damage history

3 Owners since new

No corrosion

Complete log since new

Certificate noise

## PERFORMANCE

ROBERTSON

SHORT TAKE OFF AND LANDING SYSTEM

INTERCONNECTION OF THE AILERON AND WING FLAPS SYSTEM

### CRUISE SPEED (kts.)

75% POWER		ALT. 2000 Ft			SPEED 157 kts

75% POWER		ALT. 27000 Ft		SPEED 192 kts

### FUEL CONSUMPTION

75% POWER		GPH 16

65% POWER		GPH 13

45% POWER		GPH 11

- BEST RATE OF CLIMB		Fpm 930

- TAKE OFF GROUND ROLL	Ft 1000

- LANDING GROUND ROLL	Ft 700

- STALL SPEED			54 KIAS

IMAGES