| General Specifications |
| --- |
| Year | 1989 |
| Manufacturer | PIPER |
| Model | PA-28R-201T |
| Price | € 185.000 |
| Location | Venegono (VA) |
| Conditions | Always hangared & Brand New Engine Only 40Hrs |
| Serial Number | 2803004 |
| Registration Number | I-NEWA |
| Total Time Time since Overhaul (year) | 5200 40 (engine completely substituted 2008) Brand New. |
| Number Of Seats (total) | 4 |
| MaximuM Take Off Weight | 1.315 kg |

General Information

Well maintained, always hangared, nicely fully IFR equipped Piper PA28 Turbo Arrow. A brand new engine with only 40Hrs (completely substituted in summer 2008) and avionics, makes of this Piper the best choice for flight schools or pilots whom like to have very nice navigation resources for IFR and VFR flights. The EHSI (Sandel 3525: with map, rose, arc mode ) and the StormScope (Wx-500) are completely interfaced with the GPS Garmin GNS 430. Autopilot coupled with the GPS navigation, ALT, HDG, NAV, APP functions available. Best speed at FL150 180Kts TAS Normal Cruise Speed at FL110 150Kts TAS Range 65% power 860Nm Max ceiling 20'000ft

Detailed Description

Engine Specs: CONTINENTAL TELEDYNE TSIO-360-FB 12 , N.318034, 200 HP TURBO CHARGED, Only 40 Hrs Prop(s): PROP TYPE BHC-C27F-18F, HARTZELL N.C. AM2989 2-bladed Avionics/Radios: R/T VHF NAV-ILS KING KX 155; IND NAV-ILS KING KI 209; ADF KING K R 87; AUDIO PANEL MB KING KMA 24 ATC XPDR KING KT 76 A A/P (AUTOPILOT) KING KAP 150 ELT NARCO ELT 10 ALT.ENCODER NARCO AR 850 VHF N/C/GPS GARMIN 430 97106103 E-HSI SANDEL 3525 SN 3308 (more infos on http://www.sandel.com) GPS ANTENNA GARMIN GA 56 ARM 95,3 STORMSCOPE WX-500 INTERFACED ON GARMIN GNS 430 Additional Equipment: INTERCOM HEADSETS X 4 DOUBLE ALTIMETER AIRSPEED INDICATOR TURN COORDINATOR VERTICAL SPEED INDICATOR ELETTRIC PITCH TRIM MANUAL YAW TRIM AVIONIC MASTER STBY VACUUM SUCTION STARTING PRIMER LINKED TO MAIN ELETTRIC FUEL PUMP ELT CLOCK STOPWATCH SUNVISORS Exterior: White & blue stripes, well maintained Interior: Original, well maintained and cleaned. Contact: Adriano Suella E-mail a.suella@gmail.com Mobile +39.329.096.2122