| General Specifications |
| --- |
| Year | 1964 |
| Manufacturer | Piper |
| Model | PA24-260 Fuel injection |
| Price | €57.000,00 |
| Location | Roma-Urbe |
| Conditions | Good |
| Serial Number | 4048 |
| Registration Number | I-CCWW |
| Total Time Time since Overhaul (year) | 2.200 150 hrs. since Top overhaul with new “Millennium special cast” cylinders |
| Number Of Seats (total) | 4 |
| MaximuM Take Off Weight | 2.900 lbs |

General Information

Totally Factory Primed, repainted 2002, grey leather seats, sides and ceiling new 2002 engine Top overhaul, new - Millennium special cast - steel cylinder, most original instrumentation.

Detailed Description

Engine Specs: Lycoming IO-540 260 hp engine, TSOH: 1000 hrs 150 hrs since Top overhaul with Millennium cast steel cylinders. Prop(s): Two blade propeller. Last overhaul 05/2009. Avionics/Radios: King KMA24 Audio Panel with Marker Beacon 2 x King KX165 NAV-COM 760 Channels, FM Immune Garmin 100 GPS King KR87 Digital ADF King KT76A Mode C Transponder Shadin digital fuel flow JPI 700 engine analyzer 70 Amp alternators. Replaced in 2010 406 MHz ELT with GPS & panel control NO DME! Autopilot: Altimatic II (inoperative-need check) Additional Equipment: Intercom x 2 Altimeter x 2 Anemometer Slip & turn Variometer Heated Pitot Vertical trim electric Horizontal trim Avionic Master Vacuum Lighter plug X other GPS Sunscreen MTOW: 1315 kg (2900 lbs) 4 new fuel cells recently replaced. Electric fuel pump recently replaced. Ignition harness replaced in 2010. Engine oil and fuel hoses replaced in 2010. Last 1000 hrs. inspection performed at TT: 1884 Last 500 hrs. inspection performed at TT: 2107 Gami fuel injector nozzles (below3.000 ft.@65% L.O.P. 40 liter/h 140Kt) Total fuel 90 USG usable 86 New main wheel tires NO CO-PILOT BRAKES! IFR ready. Empennage reinforcement & VNE kit New stainless steel exhaust collector pipes Door top lock improvement kit M20 engine breather oil separator Engine oil filter Kit modification Orcotek cabin sound proofing blankets 1/8th inch windows replaced in 2003. Fuel doors Key-lock Johnston aircraft high-performance wings-tips with strobe-light Johnston aircraft speed spinners Italian Luxury Tax not applicable due to aircraft age category! Exterior: painted 2002 Interior: leather seats grey, sides and ceiling new 2002 Contact: Gianfranco Ales E-mail Phone +39. 348-8620333